## Slide 1: Introduction to Fourier Neural Operators
Hilary Wu

## Slide 2: Data driven discovery of PDEs
Navier-Stokes Equation:
Estimate true values for and using PINN:
  5000 data points
  200000 epochs using Adam optimizer
  50000 iterations using L-BFGS optimizer

## Slide 4: Results
hours of training time
What if we want to predict a solution to the Navier-Stokes equation using the same parameters but different initial/boundary conditions?
Parameters | True value | Predicted value | Relative error
 | 1 | 0.99713 | 0.29%
 | 0.01 | 0.01101 | 10.07%
Parameters | True value | Predicted value | Relative error
 | 1 | 0.99713 | 0.29%
 | 0.01 | 0.01101 | 10.07%

## Slide 5: Fourier Neural Operators (FNOs)
Train a solution operator for a whole family of PDEs
Model learns
Combines linear global integral operators and non-linear local activation functions
Assuming translational invariance
Model integral operator as convolution work in Fourier space
Use Fast Fourier Transform (FFT):

## Slide 6: High level architecture
  Start from input
  Lift to higher dimension channel space by neural network P
  Apply multiple layers of integral operators and activation functions
  Project back to target dimension by neural network Q
  Output

## Slide 7: Fourier layers
Iterative update scheme:
Global path (Fourier integral operator ):
  Truncate Fourier modes to to suppress noise

## Slide 8: Improvements on PDE solutions
Burgers’ Equation:
  30% lower error rate
Darcy Flow:
  60% lower error rate
Navier-Stokes:
  30% lower error rate
  error with Reynolds number 1000
  8% error with Reynolds number 10000

## Slide 9: Application to Navier-Stokes
Estimate the solution to Navier-Stokes equation given sparse data in spatial and time domains
  Fix , parameterise
  Spatial resolution
  Time domain in 20 steps

## Slide 10: Use cases
Spectral analysis
  Truncation of Fourier modes does not limit number of modes to
  Activation function and decoder Q can recover high frequency modes
  For , truncating analytic solution to 20 modes gives 2% error
  FNO recovers solution with error when only using 12 modes
Zero-shot super-resolution
  FNO can identify high frequency patterns
  Train operator on low resolution data and evaluate at a higher resolution
  Trained FNO-3D model on resolution data
  Able to transfer to resolution

## Slide 11: Use cases
Non-periodic boundary conditions
  Traditional Fourier methods only work with periodic boundary conditions
  Linear transform W in the local path of Fourier layers enforces non-periodicity
Bayesian Inverse Problems
  Inferring parameters from observed data while quantifying uncertainty
  per evaluation using FNO compared to pseudo-spectral methods
  Total training time:
  FNO can predict solutions for different initial conditions and observations

## Slide 12: Thank for listening